Electrogovernor Use:

- Lightbar Master switch (in cab) must be on.

- Manual Mode: no minimum pressure. Expect 3 second response delay.

- Automatic Mode: 60 psi manifold pressure. minimum. Above 100 psi expect 6 sec delay and 5 psi steps.

- Not recommended for use with CAFS.

- Pressure sensor is near relief valve: flush often.