To Use the Relief Valve:

- Start with Relief Valve lever OFF

- Open Pressure Relief Shutoff (near 2 ½ discharge lever)

- Run pump and discharge at desired pressure

- Turn Relief Valve lever ON

- If pressure drops (OPEN light should come on), turn Pressure Relief Adjustment knob clockwise (CW) until pressure returns to desired set point.

- If pressure does not drop (CLOSED light), turn Pressure Relief Adjustment knob counterclockwise (CCW) until pressure drops (OPEN light) 5 to 10 psi. Then reverse knob CW slowly to return to set pressure (CLOSED light)