## Skill Sheet: Quick Attack

Objective

Squad will make a successful fire attack on the first floor of the burn building using booster tank water. Cones will simulate fire. Arrival conditions will be described on arrival.

| Arrival |
| --- |
| Position apparatus correctly |  |
| Scene size-up |  |
| Give arrival report (type of structure, fire status, exposures, quick attack mode -- do not establish command) |  |
| Prepare for fire attack |
| Communicate action plan to team |  |
| Don SCBA |  |
| Tools/Equipment - forcible entry tool, light, radio |  |
| Radio on proper frequency |  |
| Hoseline correctly deployed to entry door |  |
| Charge line |  |
| Check stream pattern and pressure ("right to fight", "left to live") |  |
| Buddy check |  |
| Enter building |
| Position squad away from swing of door |  |
| Notification of entry |  |
| Air on |  |
| Check door for heat and open slowly |  |
| Advance hoseline and attack |
| Proper line advancement and nozzle position |  |
| Crew positioned with line before entering fire room. Stay in communication with team at all times. |  |
| Check door for heat |  |
| Execute fire attack. Recheck stream pattern and direct straight stream at base of fire. |  |
| Perform hydraulic ventilation |  |
| Notification that fire is extinguished |  |
| Notification that all squad members clear of building |  |