Structure Defense Checklist

- Size Up & Strategy

- Structure Defense using Engine, Structure Defense Kit, Burning Out

- Fire Weather & LCES

- Structure Triage

1a.  Size-Up:  Know how to report a size-up

- Location:  location & address, including road names, junctions, intersections, township, range and section location using topo map

- Structures Threatened:  number of structures being threatened

- Access:  best access

- Size:  size of fire

- Fuel Types:  what the fire is in and what fuels it is heading to

- Fire Behavior:  running; creeping; spotting; torching (# of trees); crowning; rate of spread – how fast is fire moving – ok to give relative to feet per minute or per hour; direction fire is heading -- north/south etc. …uphill/downhill

- special instructions

  - staging

  - are structures threatened within next hour?

  - historic structures or old mine areas?

  - evacuation request? (draw a circle around the area effected and give road boundaries to communications)

  - hazards

    - personal vehicle blocking the road

    - smoke obstructing the road

    - homeowners leaving

    - lpg tanks, explosives, high voltage power lines

1b.  Strategy:  Know what you are going to do and why:  Form a Plan

- Main goal = life safety and personal property

- Lookout: spread, spotting, fire activity in critical zone, is ground smoking?

- What resources are available:  Can you adjust your plan to fit?

- What is first area threatened?

- Attack:  Offensive or Defensive, Direct or Indirect

- Tactical objectives – we’re going to save these 7 houses…

- Life Safety issues

- What resources are needed:  2nd tone from 4mile?, water tenders, engines, handcrews – request resources in addition to 4mile

- Where are you requesting resources from…how long will they take to get there

- Structure Defense:  Know how to defend a house and when to leave safely

- Different tools available:

  - Water (with CAFS, Batch-Mixed Surfactant)

  - Barricade

  - Hand Line

  - Wet Line

  - Burning Out

  - Homeowner’s tools

- Keep minimum of 100 gallons of water for personal safety

- Progressive hose lay – hose laid wet

  - Need nozzleman, hoseman, engineer

  - Anchor the wet line

  - Keep hose free of kinks

  - Lay hose so it won’t get burned

  - Place tees or wyes at regular intervals so can add lateral hose lays later

  - 2 ½” or 1 ½” hose

- Options if posted at structure with an engine:

  - Lay wet line around structure

  - Hose down house…special attention to exposures closest to fire, and eaves, overhangs, decks& side of house that isn’t directly affected now but may be affected after fire passes & radiant heat gets trapped on uphill side of house

- Options if left at structure without an engine:  You will always have water

  - Structure kit - has pumpkin, pump, hose, and duffel bag with appliances.  You can dig a wet line around the house, wet down the house

  - Burn out with wet line

Burning Out:  Know how and when to burn out around a house.  Know which firing tools to use and when to use them.

- Need water source

- Need 3 people:  fireman, waterman, lookout

- Radio

- LCES

- Burn out in strips, moving out from house

- Fire Weather & LCES:  Know how to use the belt weather kit; how to get pertinent   information from the Colorado weather forecast; how to report weather.  Know the LCES safety terms and how to use them.

Use belt weather kit to determine:

- Temperature

- Relative Humidity

- Wind direction/speed

- Check with IC re: frequency you will use to monitor and report weather

- Monitor NOAA weather channel

- Ask Communications for weather forecast updates

- Determine your approximate elevation (GPS unit in B-1 & T1) or request that communications provide you with GPS that matches house address

- Record date, location elevation, aspect etc. in log book

- Report on trends

LCES:  Know the LCES system and how to use it

- Lookout – experienced people at strategic sites who can see fire and where people are working.  Reports back to command

- Communications – everyone knows which radio frequencies are being used and radios are distributed among people

- Escape Routes – what are your 2 escape routes, have you marked them, does everyone know them and can everyone use them

- Safety Zones – what is the safety zone, how do you get there and when do you go there

- Structure Triage:  Know how to do an exterior and interior search and how to determine if you can save the house.

Location & Conditions to watch out for:

  - House located on a saddle or ridge

  - One-way road -- no alternate access out

  - Wood shake roof or heavy fuel loading around house

  - Fire Behavior changing due to time of day or change in weather

Exterior  Search & Report:  “I have…”

- single structure with a ____ roof type (wood, stucco, asphalt shingles)

- well-mitigated structure…or grass/slash/trees up against the house

- located propane tank and turned it off  – if you can’t find it…maybe they heat with coal, electricity, fuel oil – ask homeowner or base

- power line nearby

- cistern or other water source

- main fire threat to this house is…

Interior search

- close doors

- close windows and skylights

- close heavy drapes

- pull up light flashy curtains

- remove Venetian blinds

- move other flammable items away from windows

- board up windows closest to fire with plywood if available

- close garage doors

- turn off power at main power box (leave on 220 for well)

- turn front porch light on

- leave note

- report when done

General Considerations:  Know how to get to a house safely

  - Drive with headlights on

  - Be aware of homeowners and their emotional state

  - Prepare for homeowners evacuating as you arrive.  How will you handle this traffic?