Burning Out

Know how and when to burn out around a house.  Know which tools to use and when to use them.

Tools:

- Fusees

- Drip torch

- Homeowner’s extra fuel

- Lighter/matches

What you will need:

- Water source and hose - use homeowner’s garden hose (if power available) – otherwise you

will need a pump and fuel or backpack pumps

- 3 people:

  - fireman

  - waterman/pump engineer/hoseman

  - lookout

- Radio

- LCES

- Burn out in strips, moving out from house…3 feet, 6 feet, 9 feet etc. Don’t burn more than you can control at a time. Make sure burn is extinguished when done.

You may need to:

- Remove ladder fuels or high weeds near house

- Cut down trees, brush near house if time permits and saw team is available

- Remove combustibles (woodpiles, tarps, leaves etc.) from house

Firing Tools:

- Drip Torch (on B1, T1) with fuel

  - Use anywhere

  - Wear gloves and hold torch by handle

  - Carry upright until ready to use

  - Extinguish when not in use

- Fusee

  - Use only on grasses

  - When igniting, turn your face away and strike away from your body

  - Phosphorous material is extremely hot (1,400° F. and drips easily when burning)

  - Avoid breathing smoke and vapors from the fusee

  - Do not stare at the burning tip of the fusee; it can damage your eyes

  - Keep the fusee on the fuel you really want to burn

Goal:

Create larger, safer defensible space around house.